## Slide 1
Project Group Number:16
Project Member1: Pauskar Sunil Umesh Roll No.: MBC-45
Project Member 2: More Vikas Harishchandra Roll No.: MBC-23
Project Member 3: Pise Chaitali Kushaba Roll No.: MBC-02
Project Member 4: Ssonawane Adeeth Ankushrao Roll No.: MBD-34
Project Guide: Prof.Y.S. Khairnar
Material Optimization and Vibrational Analysis of Tie Rod

## Slide 2: Problem Statement
For competitive racing wagon i.e. go kart we need to improve efficiency of vehicle with optimum weight. By studying on steering system we found that we can reduce weight of kart also can improve efficiency.

## Slide 3
Problems Faced:-
Weight Reduction
Failure of component
Torque requirement

## Slide 4: Objectives of Project
Study of various parameter resulting in Tie Rod
Theoretical analysis of component
To enhance knowledge related to CAD and CAE Software
To do experimentation and acquire knowledge related to FFT Analyzer setup
Weight reduction in the component
To improve safety for personnel

## Slide 5: Introduction
Part of steering mechanism (Slender structural)
Capable of carrying Compressive Loads only.

## Slide 6: Steering System of Go-kart
Requirements:-
Simple, lightweight and easily operated steering system.
100% Ackerman steering.
The need of directional stability of our vehicle
To provide directional control of the vehicle with minimum input.

## Slide 7
Weight Reduction
Life of system
Improve Vibration Capacity
Part Selected:-
Tie Rod (Both Sided)
Improvement needed in Steering system

## Slide 8: Methodology
Selection of component
Collecting information
Theoretical calculation
Manufacturing and Machining
Analysis of part
To make Cad part
Documentation work
Experiment on FFT Analyzer
Result and Conclusion

## Slide 9: Old Tie Rod
Material – Mild steel
Specification
Tie rod Parameter | Dimension
Length | 250 mm
Diameter | 12 mm
Length | 30 mm
Parameter | Units | Values
Young's Modulus | (GPa) | 210
Yield Strength | (MPa) | 172-250
Tensile strength | (MPa) | 400
Poisson's Ratio |  | 0.3
Melting Point | (Deg) | 1538
Density | (g/cm*3) | 7.85

## Slide 10: Cad part of Tie rod

## Slide 11: Calculation
A) Theoretical Calculation
I. Force Calculation of Old Tie Rod:- (For Mild Steel )
Working Strength of Tie Rod = *
Yield Strength of Mild Steel ()= 250 Mpa
Assume Factor of safety(FOS) = 4
Working Stress=FOS = 250/2
=62.5 Mpa
Maximum force on Tie Rod(F)= * = 62.5*
= 8295.76 N

## Slide 12
II. Diameter calculation for New Rod:
Yield Strength of Aluminum ()= 310 Mpa
Working Strength of New Tie Rod (=/FOS= 310/4
= 77.5 Mpa
Maximum force on Tie Rod(F)=8295.76 N
Cross-Section Area of New Tie Rod (A)= =
= 107.042
Diameter of New Tie Rod= 11.67mm (Approximate 12mm)

## Slide 13
III. Natural Frequency Calculation:
For Old Tie Rod (Mild Steel):
Specification of Old Rod:-
Diameter of Rod :- 12 mm = 12*m
Modulus of Elasticity:- 210*N/m
Density of Mild Steel :- 7850 kg/
Length of Rod :- 250mm= 250*m
Moment of Inertia= == 1.0178*
Cross Section Area= 1.13097*

## Slide 14
Natural Frequency Calculation :-
=
=872.776 rad/sec.
So,
=
= 138.90 Hz.

## Slide 15
For New Tie Rod (Aluminum):
Specification of New Rod:-
Diameter of Rod :- 12 mm = 12*m
Modulus of Elasticity:- 70*N/m
Density of Mild Steel :- 2700 kg/
Length of Rod :- 250mm= 250*m
Moment of Inertia= = = 1.0178*
Cross Section Area= 1.13097*

## Slide 16
Natural Frequency Calculation :-
=
=859.23 rad/sec.
So,
=
= 136.75 Hz.

## Slide 17: New Tie Rod
Material - Aluminum
Parameter | Units | Values
Young's Modulus | (GPA) | 69
Yield Strength | (MPA) | 275
Tensile strength | (MPA) | 125
Poisson's Ratio |  | 0.3
Melting Point | (deg) | 660.3
Density | (g/cm*3) | 2.7
Specification
Tie rod | Dimension
Length | 250 mm
Diameter | 12 mm
Tie End | 
Length | 30 mm

## Slide 18
Manufacturing

## Slide 19: Fixture for experimental setup
: Fixture for MS tie rod
Fixture for Aluminium tie rod :

## Slide 20: Apparatus
Data acquisition system with amplifiers
Impact Hammer With Load Sensor
Accelerometer

## Slide 21: Experimental setup

## Slide 22: Experimental analysis
Mild Steel

## Slide 23
Aluminum

## Slide 24: Static Analysis of Cad parts
Mild steel
Aluminum

## Slide 25: Modal Analysis
A modal analysis is a technique used to determine the vibration characteristics of structures:
• natural frequencies
• mode shapes
Benefits of modal analysis:
Allow to design to resonant vibrations
Idea of design respond to different dynamic loads
Helps in calculating solution control

## Slide 26: Modal Analysis of CAD Parts
Mild steel
Aluminum

## Slide 27: Results
I. Weight Reduction
Sr. No. | Material | Weight (kg)
1 | Mild Steel | 0.2055
2 | Aluminum | 0.0705
Weight Reduction in %
% of Weight Reduction=
=100
= 65.69

## Slide 28
II. Natural Frequency
Sr no. | Material | Mode | Theoretical (Hz) | Experimental (Hz) | % of Error
1 | Mild Steel | 1 | 138.90 | 136.7 | 1.5
2 | Aluminum | 1 | 136.75 | 136.72 | 0.02
III. Cost of Material
Sr.No. | Material | Cost per Kg
1 | Mild Steel | Rs. 130
2 | Aluminum | Rs. 220

## Slide 29: Advantages and limitation of Project
Advantages:-
Weight Reduction up to 66%
Increase the efficiency and torque requirement
Limitation
Cost is little bit more

## Slide 30: Thank you